## Slide 1
Waleed Alkohlani1, Jeanine Cook2, Nafiul Siddique1
1New Mexico Sate University
2Sandia National Laboratories
Insight into Application Performance Using Application-Dependent Characteristics

## Slide 2: Introduction
Carefully crafted workload performance characterization
  Insight into performance
  Useful to architects, software developers and end users
Traditional performance characterization
  Primarily use hardware-dependent metrics
    CPI, cache miss rates…etc
  Pitfall?

## Slide 3: Overview
Define application-dependent performance characteristics
  Capture the cause of observed performance, not the effect
    Knowing the cause, one can possibly predict the effect
  Fast data collection (binary instrumentation)
Apply characterization results to:
  Gain insight into performance
    Better explain observed performance
  Understand app-machine characteristic mapping
  Benchmark similarity and other studies

## Slide 4: Outline
Application-Dependent Characteristics
Experimental Setup
  Platform, Tools, and Benchmarks
Sample Results
Conclusions & Future Work

## Slide 5: Application-Dependent Characteristics
General Characteristics
  Dynamic instruction mix
  Instruction dependence (ILP)
  Branch predictability
  Average instruction size
  Average basic block size
  Computational intensity
Memory Characteristics
  Data working set size
    Also, timeline of memory usage
  Spatial & Temporal locality
  Average # of bytes read/written per mem instruction
These characteristics still depend on ISA & compiler!

## Slide 6: General Characteristics: Dynamic Instruction Mix
Ops vs. CISC instructions
  Load, store, FP, INT, and branch ops
Measured:
  Frequency distributions of the distance between same-type ops
    Frequency distributions
    Ld-ld, st-st, fp-fp, int-int, br-br…
Information:
  Number and types of execution units
Chart: Int-Int Distance
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | . | . | . | 512
% of total Ops | 0 | 35 | 10 | 5 | 2.5 | 0 | 0 | 0.8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7: General Characteristics:
Instruction dependence (ILP)
  Measured:
    Frequency distribution of register-dependence distances
      Distance in # of instrs between producer and consumer
    Also, inst-to-use (fp-to-use, ld-to-use, ….)
  Information:
    Indicative of inherent ILP
    Processor width, optimal execution units…
Branch predictability
  Measured:
    Branch Transition Rate
      % of time a branch changes direction
      Very high/low rates indicate better predictability
      11 transition rate groups (0-5%, 5-10%...etc)
  Information:
    Complexity of branch predictor hardware required
    Understand observed br misprediction rates

## Slide 8: General Characteristics:
Average instruction size
  Measured:
    A frequency distribution of dynamic instr sizes
  Information:
    Relate to processor’s fetch (and dispatch) width
Average basic block size
  Measured:
    A frequency distribution of basic block sizes (in # instrs)
  Information
    Indicative of amount of exposed ILP in code
    Correlated to branch frequency
Computational intensity
  Measured:
    Ratio of flops to memory accesses
  Information:
    Indirect measure of “data movement”
    Moving data is slower than doing an operation on it
    Should also know the # of bytes moved per memory access
      Maybe re-define as # flops / # bytes moved?

## Slide 9: Memory Characteristics:
Working set size
  Measured:
    # of unique bytes touched by an application
  Information:
    Memory size requirements
    How much stress is on memory system
  Timeline of memory usage

## Slide 10: Memory Characteristics:
Temporal & Spatial Locality
  Information:
    Understand available locality & how cache can exploit it
      How effectively an app utilizes a given cache organization
    Reason about the optimal cache config for an application
  Measured:
    Frequency distributions of memory-reuse distances (MRDs)
    MRD = # of unique n-byte blocks referenced between two references to the same block
      16-byte, 32-byte, 64-byte, 128-byte blocks are used
      One distribution for each block size
      Also, separate distributions for data, instruction, and unified refs
  Due to extreme slow-downs:
    Currently, maximum distance (cache size) is 32MB
    Use sampling (SimPoints)

## Slide 11: Memory Characteristics: Spatial Locality
Goal:
  Understand how quickly and effectively an app consumes data available in a cache block
  Optimal cache line size?
How:
  Plot points from MRD distribution that correspond to short MRDs: 0 through 64
    Others use only a distance of 0 and compute “stride”
Problem:
  In an n-way set associative cache, the in-between references may be to the same set
Solution:
  Look at % of refs spatially local with d = assoc
  Capture set-reuse distance distribution!
    Must know cache size & associativity
HPCCG

## Slide 12: Memory Characteristics: Temporal Locality
Goal:
  Understand optimal cache size to keep the max % of references temporally local
  May be used to explain (or predict) cache misses
How:
  Plot MRD distribution with distances grouped into bins corresponding to cache sizes
  Very useful in fully (highly) assoc. caches
Problem:
  In an n-way set associative cache, the in-between references may be to the same set
Solution:
  Capture set-reuse distance distribution!
    Must know cache size & associativity
    Short MRDs, short SRD’s  good?
    Long MRDs, short SRD’s  bad?
    Long SRD’s?
HPCCG

## Slide 13: Experimental Setup
Platform:
  8-node Dell cluster
    Two 6-core Xeon X5670 processors per node s(Westmere-EP)
    32KB L1 and 256KB L2 caches (per core), 12MB L3 cache (shared)
Tools:
  In-house DBI tools (Pin-based)
  PAPIEX to capture on-chip performance counts
Benchmarks:
  Five SPEC MPI2007 (serial versions only)
    leslie3d, zeusmp2, lu (fluid dynamics)
    GemsFDTD (electromagnetics)
    milc (quantum chromodynamics)
  Five Mantevo benchmarks (run serially)
    miniFE (implicit FE) : problem size  (230, 230, 230)
    HPCCG (implicit FE) : problem size (1000, 300, 100)
    miniMD (molecular dynamics) : problem size  lj.in (145, 130, 50)
    miniXyce (circuit simulation) : input  cir_rlc_ladder50000.net
    CloverLeaf (hydrodynamics) : problem size  (x=y=2840)

## Slide 14: Sample Results
Instruction Mix
Computational Intensity

## Slide 15: Sample Results (ILP Characteristics)
SPEC MPI shows better ILP (particularly w.r.t memory loads)

## Slide 16: Sample Results (Branch Predictability)
miniMD seems to have a branch predictability problem

## Slide 17: Sample Results (Memory)
Data Working Set Size
Avg # Bytes per Memory Op

## Slide 18: Sample Results (Locality)
In general, Mantevo benchmarks show
  Better spatial & temporal locality

## Slide 19: Sample Results (Hardware Measurements)
Cycles-Per-Instruction (CPI)
Branch Misprediction Rates

## Slide 20: Sample Results (Hardware Measurements)
L1, L2, and L3 Cache Miss Rates

## Slide 21: Conclusions & Future Work
Conclusions:
  Application-dependent workload characterization
    More comprehensive set of characteristics & metrics
      Independent of hardware
    Provides insight
  Results on SPEC MPI2007 & Mantevo benchmarks
    Mantevo exhibits more diverse behavior in all dimensions
Future Work:
  Characterize more aspects of performance
    Synchronization
    Data movement

## Slide 22: Questions